## Slide 1
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Find the range of addresses in the following blocks.
123.56.77.32/29
180.34.64.64/30
200.17.21.128/27
17.34.16.0/23
Solution:
123.56.77.32 ~ 123.56.77.39
180.34.64.64 ~ 180.34.64.67
200.17.21.128 ~ 200.17.21.159
17.34.16.0 ~ 17.34.17.255

## Slide 2
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
What is the network address if one of the addresses is 167.199.170.82/27?
Solution:
167.199.170.64/27
Explanation:
Prefix length: 27, then 32-27=5.
The 5 bits affect only the last byte. The last byte is 01010010.
Changing the last 5 bits to 0s, we get 01000000 or 64.

## Slide 3
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
In a block of addresses, we know the IP address of one host is 25.34.12.56/16.
What are the first address (network address), first and the last usable IP address, limited broadcast address in this block?
Solution:
Network address - 25.34.0.0/16,
First address 25.34.00000000.00000001 25.34.0.1/16
Last address 25.34.11111111.11111110 25.34.255.254/16

## Slide 4
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
You are given the network address 175.200.0.0; you are required to have 4 subnets.
What is the minimum number of Host Bits can you take in to the Network Bits for this purpose?
Write down the addresses of 4 subnets. Write the subnet mask for the network.
Solution:
Network part Host part
175.200.00000000.0 175.200.0.0/18
175.200.01000000.0 175.200.64.0/18
175.200.10000000.0 175.200.128.0/18
175.200.11000000.0 175.200.192.0/18

## Slide 5
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An organization is granted the block 130.34.12.64/26. The organization needs to have four subnets. What are the subnet addresses and the range of addresses for each subnet?
Solution:
Subnet 1: 130.34.12.64/28 to 130.34.12.79/28
Subnet 2 : 130.34.12.80/28 to 130.34.12.95/28
Subnet 3: 130.34.12.96/28 to 130.34.12.111/28
Subnet 4: 130.34.12.112/28 to 130.34.12.127/28
Explanation:

## Slide 6
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Explanation:
If you make it (subnets => 22 = 4) /28, you can get four subnets with 14 usable IPs in each subnet (host => 24 = 16).
Network: 130.34.12.64/28 10000010.00100010.00001100.0100 0000
Broadcast: 130.34.12.79 10000010.00100010.00001100.0100 1111
HostMin: 130.34.12.65 10000010.00100010.00001100.0100 0001
HostMax: 130.34.12.78 10000010.00100010.00001100.0100 1110
Hosts/Network(Subnet): 14

## Slide 7
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An organization is granted the block 16.0.0.0 in Class A (or 16.0.0.0/8). The administrator wants to create 500 fixed- length subnets.
find the subnet mask
find the number of addresses in each subnet.
find the first and last address in first subnet and in the last subnet (500th subnet).
Solution:
500 subnets, 9 bits should be taken from host part.
Number of host bits remain = 15

## Slide 8
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Solution:
First address, first subnet 16.0.0.00000001 16.0.0.1
Last address, first subnet 16.0.01111111.11111110 16.0.127.254
First address, last subnet 16.11111111.100000000.00000001 16.255.128.1
Last address, last subnet 16.11111111.11111111.11111110 16.255.255.254

## Slide 9
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Solution:
There are 28 = 256 addresses in this block. First address is 14.24.74.0/24; Last address is 14.24.74.255/24.
To satisfy the third requirement, we assign addresses to subblocks, starting with the largest and ending with the smallest one.

## Slide 10
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Question: The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Solution:
Largest subblock requires 120 addresses (not power of 2), we allocate 128 addresses. The subnet mask for this subnet: 25. The first address in this block is 14.24.74.0/25 ; the last address is 14.24.74.127/25.
Number of addresses in the second largest subblock requires 60 addresses (not a power of 2), we allocate 64 addresses. The subnet mask for this subnet: 26. The first address in this block is 14.24.74.128/26; the last address is 14.24.74.191/26

## Slide 11
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Question: The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Solution:
Number of addresses in the second largest subblock requires 10 addresses (not a power of 2), we allocate 16 addresses. The subnet mask for this subnet: 28. The first address in this block is 14.24.74.192/28; the last address is 14.24.74.207/28

## Slide 12
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Find the network address and the directed broadcast address of subnetted Class B IPv4 address 172.25.171.182 with a subnet mask of 255.255.224.0.

## Slide 13
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An ISP is granted a block of addresses starting with 150.80.0.0/16. The ISP wants to distribute these blocks to 2600 customers as follows.
The first group has 200 medium-size businesses; each needs 128 addresses.
The second group has 400 small businesses; each needs 16 addresses.
The third group has 2000 households; each needs 4 addresses.
Design the subblocks and give the slash notation for each subblock. Find out how many addresses are still available after these allocations.

## Slide 14
arunvikas.singh@pes.edu
THANK YOU
Dr. Arun Vikas Singh
Department of Computer Science and Engineering