## Slide 1
COMPUTER NETWORKS
Ashwini M Joshi.
Department of Computer Science and Engineering
ashwinimjoshi@pes.edu

## Slide 2
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 3
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 4
COMPUTER NETWORKS
Network-layer Services and Protocol
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 5
COMPUTER NETWORKS
Two Key Network-layer Functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 6
COMPUTER NETWORKS
Interplay between Routing and Forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 7
COMPUTER NETWORKS
Connection Setup
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 8
COMPUTER NETWORKS
Network Service Model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?

## Slide 9
COMPUTER NETWORKS
Network-layer Service Model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees?

## Slide 10
COMPUTER NETWORKS
Network-layer Service Model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?

## Slide 11
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 12
COMPUTER NETWORKS
Router Architecture Overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 13
COMPUTER NETWORKS
Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 14
COMPUTER NETWORKS
Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
This is a really important slide
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R

## Slide 15
COMPUTER NETWORKS
Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 16
COMPUTER NETWORKS
Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 17
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 18
COMPUTER NETWORKS
Network Layer: Internet
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller

## Slide 19
COMPUTER NETWORKS
IP Datagram Format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 20
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 21
COMPUTER NETWORKS
IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 22
COMPUTER NETWORKS
IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 23
COMPUTER NETWORKS
Fragmentation – Example

## Slide 24
COMPUTER NETWORKS
Fragmentation – Example

## Slide 25
COMPUTER NETWORKS
Fragmentation – Numerical Example
An IP router with a Maximum Transmission Unit (MTU) of 200 bytes has received an IP packet of size 520 bytes with an IP header of length 20 bytes. The values of the relevant fields in the IP header.

## Slide 26
COMPUTER NETWORKS
Fragmentation – Numerical Example
An IP router with a Maximum Transmission Unit (MTU) of 200 bytes has received an IP packet of size 520 bytes with an IP header of length 20 bytes. The values of the relevant fields in the IP header.

## Slide 27
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 29
COMPUTER NETWORKS
IP addressing: Introduction
IP address: 32-bit unique ID associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 30
COMPUTER NETWORKS
IP addressing: Introduction
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Solution:
We replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 31
COMPUTER NETWORKS
IP addressing: Introduction
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Solution:
We replace each decimal number with its binary equivalent.

## Slide 32
COMPUTER NETWORKS
IP addressing: Introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Q: how are interfaces actually connected?
A: wired
Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)
A: we’ll learn about that in chapters 6, 7

## Slide 33
COMPUTER NETWORKS
Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits
A portion of a network that shares a particular subnet address.

## Slide 34
COMPUTER NETWORKS
Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 35
COMPUTER NETWORKS
Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24
A 32-bit combination used to describe which portion of an address refers to the subnet and which part refers to the host.

## Slide 36
COMPUTER NETWORKS
IP addressing: Classful Addressing

## Slide 37
COMPUTER NETWORKS
IP addressing: Classful Addressing
Class D: multicast, Class E: reserved (experimental)
Broadcast Address: 255.255.255.255
Network Masks
Class A: 255.0.0.0
Class B: 255.255.0.0
Class C: 255.255.255.0

## Slide 38
COMPUTER NETWORKS
IP addressing: Classful Subnet Masks

## Slide 39
COMPUTER NETWORKS
IP addressing: introduction
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 40
COMPUTER NETWORKS
IP addressing: Why not Classful Addressing?
Network portion - 8, 16, or 24 bits in length – known as Class A, B and C networks respectively
A class C (/24) - accommodate only up to 28 - 2 = 254 hosts (two of the 28 = 256 addresses are reserved for special use)
A class B (/16) subnet, supports up to 65,634 hosts
A class A (/8) subnet, up to 16,777,214 hosts
too small for many organizations
too large, poor utilization
Classful addressing, which is almost obsolete, is replaced with classless addressing.

## Slide 41
COMPUTER NETWORKS
IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 42
COMPUTER NETWORKS
IP addressing: CIDR

## Slide 43
COMPUTER NETWORKS
IP addressing: CIDR – Prefix Lengths
The addresses in color are the default masks for classes A, B, and C.
Thus, classful addressing is a special case of classless addressing.

## Slide 44
COMPUTER NETWORKS
IP addresses: how to get one?
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 45
IP address of one host is 25.34.12.56/16
Find the first addresses in this block.
Find the last addresses in this block.

## Slide 46
IP address of one host is 182.44.82.16/26
Find the first addresses in this block.
Find the last addresses in this block.

## Slide 47
An organization is granted the block 214.17.160.0/24. The administrator wants to create 8 subnets.
Find the subnet mask.
Find the last addresses in first subnet.
Find the first addresses in last subnet.

## Slide 48
COMPUTER NETWORKS
Hierarchical addressing: route aggregation
hierarchical addressing allows efficient advertisement of routing information:
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
The ability to use a single prefix to advertise multiple networks is often referred to as address aggregation (also route aggregation or route summarization).

## Slide 49
COMPUTER NETWORKS
Hierarchical addressing: more specific routes
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
200.23.18.0/23
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 50
COMPUTER NETWORKS
Hierarchical addressing: more specific routes
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 51
COMPUTER NETWORKS
IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 52
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 53
COMPUTER NETWORKS
DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 54
COMPUTER NETWORKS
DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 55
COMPUTER NETWORKS
DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 56
COMPUTER NETWORKS
DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 57
COMPUTER NETWORKS
DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 58
COMPUTER NETWORKS
DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 59
COMPUTER NETWORKS
IP addressing: last words…
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu, …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 60
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 Introduction to Routing Algorithms

## Slide 61
COMPUTER NETWORKS
NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 62
COMPUTER NETWORKS
NAT: Network Address Translation
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 63
COMPUTER NETWORKS
NAT: Network Address Translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 64
COMPUTER NETWORKS
NAT: Network Address Translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 65
COMPUTER NETWORKS
NAT: Network Address Translation
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 66
COMPUTER NETWORKS
NAT: Network Address Translation
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?
Solution: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 25000) always forwarded to 10.0.0.1 port 25000

## Slide 67
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 IPv6 Protocol
  4.8 Introduction to Routing Algorithms

## Slide 68
COMPUTER NETWORKS
ICMP: Internet Control Message Protocol
Used by hosts and routers to communicate network-layer information.
Typical use of ICMP is for error reporting.
Eg: “Destination network unreachable”
ICMP messages – carried as IP payloads.
ICMP is often considered part of IP, but architecturally it lies just above IP.
ICMP messages have a type and a code field.
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 69
COMPUTER NETWORKS
ICMP: Internet Control Message Protocol
Perform – Network diagnostics
Utilities traceroute and ping – use ICMP.
Other examples of ICMP messages:
  Source quench message (congestion)
  Parameter problem (bad IP header)
  Time exceeded message (TTL)
  Destination unreachable
  Redirection message

## Slide 70
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 IPv6 Protocol
  4.8 Introduction to Routing Algorithms

## Slide 71
COMPUTER NETWORKS
Introduction to IPv6
128 bits address
340 undecillion address (340 + 33 digits)
IPv6 address apace is 296 times of the IPv4 address.
Made up of eight 16-bit blocks (octet)
Separated by ‘:’
Hexadecimal, each hexadecimal character – 4 bits
Rules:
Discard leading Zero(es)
If two of more blocks contain consecutive zeroes, omit them all and replace with double colon sign ::
340,282,366,920,938,463,374,607,431,768,211,456

## Slide 72
COMPUTER NETWORKS
Introduction to IPv6
Colon hexadecimal notation
Zero compression
CIDR address
Rule 1
Rule 2

## Slide 73
COMPUTER NETWORKS
IPv6 Addressing
Show the unabbreviated colon hex notation for the following IPv6 addresses:
a. An address with 64 0s followed by 64 1s.
b. An address with 128 0s.
c. An address with 128 1s.
d. An address with 128 alternative 1s and 0s.
Solution
a. 0000:0000:0000:0000:FFFF:FFFF:FFFF:FFFF
b. 0000:0000:0000:0000:0000:0000:0000:0000
c. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
d. AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA

## Slide 74
COMPUTER NETWORKS
IPv6 Addressing
The following shows the zero contraction version of addresses in previous example.
a. :: FFFF:FFFF:FFFF:FFFF
b. ::
c. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
d. AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA

## Slide 75
COMPUTER NETWORKS
IPv6 Addressing
Show abbreviations for the following addresses:
a. 0000:0000:FFFF:0000:0000:0000:0000:0000
b. 1234:2346:0000:0000:0000:0000:0000:1111
c. 0000:0001:0000:0000:0000:0000:1200:1000
d. 0000:0000:0000:0000:0000:FFFF:24.123.12.6
Solution
a. 0:0:FFFF::
b. 1234:2346::1111
c. 0:1::1200:1000
d. ::FFFF:24.123.12.6

## Slide 76
COMPUTER NETWORKS
IPv6 Addressing
Decompress the following addresses and show the complete unabbreviated IPv6 address:
a. 1111::2222
b. ::
c. 0:1::
d. AAAA:A:AA::1234
Solution
a. 1111:0000:0000:0000:0000:0000:0000:2222
b. 0000:0000:0000:0000:0000:0000:0000:0000
c. 0000:0001:0000:0000:0000:0000:0000:0000
d. AAAA:000A:00AA:0000:0000:0000:0000:1234

## Slide 77
COMPUTER NETWORKS
Three Address Types
In IPv6, a destination address belong to:
  Unicast Address (one-to-one) – defines a single interface (computer or router)
  Multicast Address (one-to-many) – also defines a group of computers, each member of the group receives a copy.
  Anycast Address (one-to-nearest) – defines a group of computers that all share a single address.
  Broadcast Address (one-to-all) – ×

## Slide 78
COMPUTER NETWORKS
Address Space Allocation

## Slide 79
COMPUTER NETWORKS
Address Space Allocation
Figure shows that only a portion of the address space can be used for global unicast communication.
How many addresses are in this block?
Solution
This block occupies only one-eighth of the address spaces. To find the number of addresses, we can divide the total address space by 8 or 23 . The result is (2128)/(23) = 2125 —> a huge block.

## Slide 80
COMPUTER NETWORKS
Algorithm for finding the allocated blocks

## Slide 81
COMPUTER NETWORKS
Assigned and Reserved Blocks
The unspecified address in IPv6 is ::/128. It should never be used as a destination address.
The loopback address in IPv6 is ::1/128. It should never be used as a destination address.

## Slide 82
COMPUTER NETWORKS
Assigned and Reserved Blocks
Embedded IPv4 Addresses – Compatible Address.
CIDR notation is ::/96.
(Ipv6 -> IPv6)
Embedded IPv4 Addresses – Mapped Address.
(Ipv6 -> IPv4)

## Slide 83
COMPUTER NETWORKS
Assigned and Reserved Blocks
Unique local unicast block
Private Addressing in IPv6 – Site level & Link level
Link local block

## Slide 84
COMPUTER NETWORKS
Assigned and Reserved Blocks
Multicast address - used to define a group of hosts instead of just one.

## Slide 85
COMPUTER NETWORKS
Global Unicast Addresses
Used for unicast (one-to-one) communication between two hosts in the Internet.
CIDR notation for the block is 2000::/3 - three leftmost bits are the same for all addresses (001).
Three Levels of Hierarchy:
  Global Routing Prefix
  Subnet identifier
  Interface identifier
Global unicast address
Recommended Length of Different Parts in Unicast Addressing

## Slide 86
COMPUTER NETWORKS
Global Unicast Addresses
  Global Routing Prefix –> 3 bits (001) + 45 bits = 245 sites (ISP/private org)
  Subnet identifier –> 216 = 6553 subnets
  Interface identifier –> similar to Host ID in IPv4 (IP level & physical level are different),
    Physical address is 48 bits while the hostid is less than 32 bits
    Embed physical address (<64 bits) into Interface ID – whole/part
    Two physical addressing scheme :
      64-bit extended unique identifier (EUI-64) defined by IEEE &
      48-bit physical address defined by Ethernet.

## Slide 87
COMPUTER NETWORKS
Global Unicast Addresses
Mapping for EUI-64
Mapping for Ethernet MAC (48 bits)

## Slide 88
COMPUTER NETWORKS
Global Unicast Addresses
Find the interface identifier if the physical address in the EUI is
(F5-A9-23-EF-07-14-7A-D2)16 using the format we defined for Ethernet addresses.
Solution
We only need to change the seventh bit of the first octet from 0 to 1 and change the format to colon hex notation.
The result is F7A9:23EF:0714:7AD2.
2. Find the interface identifier if the Ethernet physical address is
(F5-A9-23-14-7A-D2)16 using the format we defined for Ethernet addresses.
Solution
We only need to change the seventh bit of the first octet from 0 to 1, insert two octet FFFE16 and change the format to colon hex notation.
The result is F7A9:23FF:FE14:7AD2 in colon hex.

## Slide 89
COMPUTER NETWORKS
Global Unicast Addresses
An organization is assigned the block 2000:1456:2474/48. What is the CIDR notation for the blocks in the first and second subnets in this organization?
Solution
Theoretically, the first and second subnets should use the block with subnet identifier 000116 and 000216. This means that the blocks are
2000:1456:2474:0000/64 and 2000:1456:2474:0001/64.
An organization is assigned the block 2000:1456:2474/48. What is the IPv6 address of an interface in the third subnet if the IEEE physical address of the computer is (F5-A9-23-14-7A-D2)16?
Solution
The interface identifier is F7A9:23FF:FE14:7AD2. If we add this identifier to the global prefix and the subnet identifier, we get: 2000:1456:2474:0002:F7A9:23FF:FE14:7AD2/128

## Slide 90
COMPUTER NETWORKS
Autoconfiguration
  In IPv6, a host can also configure itself (DHCP can still be used to allocate an IPv6 address to a host.)
    The host first creates a link local address for itself.
      10-bit link local prefix (1111 1110 10) + 54 zeros + 64-bit interface identifier.
    The host then tests to see if this link local address is unique.
      64-bit interface identifier is supposed to be unique (high probability)
      To confirm, sends a neighbor solicitation message, and waits for neighbor advertisement message. Fails -> DHCP.
    Pass -> host stores this address as its link-local address (for private communication), prepare its global unicast address.
      Sends a router solicitation message, receives a router advertisement message

## Slide 91
COMPUTER NETWORKS
Global Unicast Addresses
Assume a host with Ethernet address (F5-A9-23-11-9B-E2)16 has joined the network. What would be its global unicast address if the global unicast prefix of the organization is 3A21:1216:2165 and the subnet identifier is A245?
Solution
The host first creates its interface identifier as F7A9:23FF:FE11:9BE2
using the Ethernet address read from its card, the host then creates its link-local address as: FE80::F7A9:23FF:FE11:9BE2
Assuming that this address is unique, the host sends a router solicitation message and receives the router advertisement message that announces the combination of global unicast prefix and the subnet identifier as 3A21:1216:2165:A245:1232.
The host then appends its interface identifier to this prefix to find and store its global unicast address as: A21:1216:2165:A245:F7A9:23FF:FE11:9BE2

## Slide 92
COMPUTER NETWORKS
Renumbering
  Renumbering of the address prefix (n) is built in IPv6 - to allow sites to change the service provider.
  Each site – prefix by service provider.
  If the site changes provider, address prefix need to be changed.
  Router – assign new prefix, use the existing prefix for a short time before disabling it (two prefixes – during transition time).
  Next Generation DNS – under study.

## Slide 93
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 IPv6 Protocol
  4.8 Introduction to Routing Algorithms

## Slide 94
COMPUTER NETWORKS
IPv6 Protocol: Rationale for Change
  Larger address space
  Better header format
  New options
  Allowance for extension
  Support for resource allocation
  Support for more security
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
fragmentation/reassembly: no

## Slide 95
COMPUTER NETWORKS
IPv6 Datagram Format
Format of the base header

## Slide 96
COMPUTER NETWORKS
Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?

## Slide 97
COMPUTER NETWORKS
Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)

## Slide 98
COMPUTER NETWORKS
Tunneling and Encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 99
COMPUTER NETWORKS
Tunneling and Encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 100
COMPUTER NETWORKS
Tunneling
C-to-D
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
D-to-E:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!

## Slide 101
COMPUTER NETWORKS
IPv6 Adoption
https://www.akamai.com/us/en/resources/our-thinking/state-of-the-internet-report/state-of-the-internet-ipv6-adoption-visualization.jsp

## Slide 102
COMPUTER NETWORKS
  4.1 Overview of Network Layer
  4.2 What’s Inside a Router?
  4.3 Switching
  4.4 The Internet Protocol (IP)
    Datagram format
    Fragmentation
    IPv4 addressing
    NAT
  4.5 Introduction to Network Layer Protocols
    DHCP
    ICMP
Unit – 4 Network Layer and Internet Protocol
  4.6 IPv6 Addressing
  4.7 IPv6 Protocol
  4.8 Introduction to Routing Algorithms

## Slide 103
COMPUTER NETWORKS
Introduction to Routing Algorithms

## Slide 104
COMPUTER NETWORKS
Distance Vector vs Link State
 | Distance Vector | Link State
Primary principle | Send entire routing table to its neighbors | Only provides link state information
Learning about network | Learn about network only from neighbors | Learn about network from all routers
Building the routing table | Based on inputs from only neighbors | Based on complete database collected from all routers
Advertisement of updates | Sends periodic updates every 30-90 seconds – Broadcasts updates | Use triggered updates, only when there is a change – Multicasts updates
Routing loops | Vulnerable | Less prone to routing loops

## Slide 105
COMPUTER NETWORKS
Distance Vector vs Link State
 | Distance vector | Link State
Convergence (stabilization) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Cost |  | More than Distance vector
Scalability |  | More scalable than distance vector
Examples | RIP, IGRP | OSPF, IS-IS

## Slide 106
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering