## Slide 1
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering
ashwinimjoshi@pes.edu

## Slide 2
Text Book
COMPUTER NETWORKS
Slides adapted from
Computer Networking: A Top-Down Approach Jim Kurose, Keith Ross Pearson, 2017
8th Edition

## Slide 3
COMPUTER NETWORKS
Link Layer and LAN
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 4
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 5
COMPUTER NETWORKS
Introduction to link layer
Error detection and correction techniques
  Parity Checks
  Internet Checksum
  Cyclic Redundancy Check
Class 47 : Intro to Link layer : Learning Objectives

## Slide 6
Introduction to Link layer
COMPUTER NETWORKS
link layer has responsibility of
transferring datagram from one node to physically adjacent node over a link
mobile network
enterprise
network
national or global ISP
datacenter
network
Terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired
  wireless
  LANs
layer-2 packet: frame, encapsulates datagram

## Slide 7
Datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
Each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm
Link layer : context
COMPUTER NETWORKS

## Slide 8
…
…
Link layer : services
COMPUTER NETWORKS
Framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)

## Slide 9
…
…
Link layer : services
COMPUTER NETWORKS
Reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 10
Link layer : services (more)
COMPUTER NETWORKS
Flow control:
  pacing between adjacent sending and receiving nodes
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
…
…

## Slide 11
Link layer : services (more)
COMPUTER NETWORKS
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Half-duplex and Full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…

## Slide 12
In each-and-every host
Link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
Attaches into host’s system buses
Combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
Where is the link layer implemented?
COMPUTER NETWORKS
application
transport
network
link
link
physical

## Slide 13
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
Sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
Receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram
Interfaces communicating
COMPUTER NETWORKS

## Slide 14
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 15
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram
COMPUTER NETWORKS
Error detection

## Slide 16
Single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
Two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
COMPUTER NETWORKS
Parity checking

## Slide 17
Sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment
COMPUTER NETWORKS
Internet checksum (review)

## Slide 18
More powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
Goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G.
  If non-zero remainder: error
  detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC)

## Slide 19
We want:
  D.2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
or equivalently:
  D.2r = nG XOR R
or equivalently:
if we divide D.2r by G, want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC) : example

## Slide 20
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 21
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 22
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 23
COMPUTER NETWORKS
Multiple Access Protocols-Taxonomy
Carrier Sense Multiple Access
CSMA/CD
Class 48 : Multiple Access Protocols : Learning Objectives

## Slide 24
Two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP for dial-up access
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G
COMPUTER NETWORKS
Multiple access links protocols

## Slide 25
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Multiple access protocol
COMPUTER NETWORKS
Multiple access protocols

## Slide 26
Given: multiple access channel (MAC) of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
COMPUTER NETWORKS
An ideal Multiple access protocol

## Slide 27
Three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
COMPUTER NETWORKS
MAC protocols : Taxonomy

## Slide 28
Simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist
COMPUTER NETWORKS
CSMA ( Carrier Sense Multiple Access)

## Slide 29
Collisions can still occur with carrier sensing:
  Propagation delay means two nodes may not hear each other’s just-started transmission
Collision: entire packet transmission time wasted
  Distance & propagation delay play role in in determining collision probability
spatial layout of nodes
COMPUTER NETWORKS
CSMA : Collisions

## Slide 30
CSMA/CS reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes
COMPUTER NETWORKS
CSMA / CD

## Slide 31
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
COMPUTER NETWORKS
Ethernet CSMA / CD Algorithm

## Slide 32
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!
COMPUTER NETWORKS
CSMA / CD Efficiency

## Slide 33
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 34
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 35
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 36
COMPUTER NETWORKS
Link layer Addressing
Address Resolution Protocol
Class 49 : Switched LAN : Learning Objectives

## Slide 37
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD
COMPUTER NETWORKS
MAC Addresses

## Slide 38
Each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
COMPUTER NETWORKS
MAC Addresses

## Slide 39
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached
COMPUTER NETWORKS
MAC Addresses

## Slide 40
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
COMPUTER NETWORKS
ARP : Address Resolution Protocol

## Slide 41
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)
COMPUTER NETWORKS
ARP Protocol in action

## Slide 42
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)
COMPUTER NETWORKS
ARP Protocol in action

## Slide 43
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500
COMPUTER NETWORKS
ARP Protocol in action

## Slide 44
Walkthrough: sending a datagram from A to B via R
  Focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  Assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)
    A knows R’s MAC address (how?)
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 45
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 46
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 47
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 48
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
Transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 49
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 50
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 51
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 52
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 53
COMPUTER NETWORKS
Physical Topology
Frame Structure
Class 50 : Ethernet : Learning Objectives

## Slide 54
“Dominant” wired LAN technology:
First widely used LAN technology
Simpler, cheap
Kept up with speed race: 10 Mbps – 400 Gbps
Single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters
COMPUTER NETWORKS
Ethernet

## Slide 55
Bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
Switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
COMPUTER NETWORKS
Ethernet : Physical Topology

## Slide 56
Sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
Preamble:
Used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011
COMPUTER NETWORKS
Ethernet Frame Structure

## Slide 57
dest.
address
source
address
data (payload)
CRC
preamble
type
Addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
COMPUTER NETWORKS
Ethernet Frame Structure ( more)

## Slide 58
Connectionless: no handshaking between sending and receiving NICs
Unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff
COMPUTER NETWORKS
Ethernet : Unreliable Connectionless

## Slide 59
  Different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
Many different Ethernet standards
  Common MAC protocol and frame format
  Different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
COMPUTER NETWORKS
802.3 Ethernet Standards: Link and Physical Layers

## Slide 60
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 61
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 62
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 63
COMPUTER NETWORKS
Multiple Simultaneous Transmissions
Frame Forwarding and Filtering
Class 51 : Link Layer Switches : Learning Objectives

## Slide 64
Switch is a link-layer device: takes an active role
  Store, forward Ethernet frames
  Examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent: hosts unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured
COMPUTER NETWORKS
Ethernet switch

## Slide 65
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
COMPUTER NETWORKS
Switch : Multiple Simultaneous Transmissions

## Slide 66
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  No collisions; full duplex
  Each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously
COMPUTER NETWORKS
Switch : Multiple Simultaneous Transmissions

## Slide 67
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: How does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: Each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: How are entries created, maintained in switch table?
  something like a routing protocol?
COMPUTER NETWORKS
Switch Forwarding Table

## Slide 68
A
A’
B
B’
C
C’
1
2
3
4
5
6
Switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  When frame received, switch “learns” location of sender: incoming LAN segment
  Records sender/location pair in switch table
COMPUTER NETWORKS
Switch : Self - learning

## Slide 69
When frame received at switch:
  1. Record incoming link, MAC address of sending host
  2. Index switch table using MAC destination address
  3. If entry found for destination then {
  If destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */
COMPUTER NETWORKS
Switch : Frame Filtering / Forwarding

## Slide 70
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
Frame destination, A’, location unknown:
Flood
Destination A location known:
Selectively send
on just one link
COMPUTER NETWORKS
Self-learning, Forwarding : Example

## Slide 71
Self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
COMPUTER NETWORKS
Interconnecting Switches

## Slide 72
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
COMPUTER NETWORKS
Self-learning Multi-switch Example

## Slide 73
to external
network
router
IP subnet
mail server
web server
COMPUTER NETWORKS
Small Institutional Network

## Slide 74
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-74
Both are store-and-forward:
Routers: network-layer devices (examine network-layer headers)
Switches: link-layer devices (examine link-layer headers)
Both have forwarding tables:
Routers: compute tables using routing algorithms, IP addresses
Switches: learn forwarding table using flooding, learning, MAC addresses
COMPUTER NETWORKS
Switches Vs Routers

## Slide 75
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 76
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 77
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 78
COMPUTER NETWORKS
Synthesis of web request..
Class 52 : A day in the life of a web request : Learning Objectives

## Slide 79
Our journey down the protocol stack is now complete!
  application, transport, network, link
Putting-it-all-together: synthesis!
  Goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  Scenario: student attaches laptop to campus network, requests/receives www.google.com
COMPUTER NETWORKS
Synthesis : A day in the life of a web request

## Slide 80
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
Arriving mobile client attaches to network …
Requests web page: www.google.com
Scenario:
Sounds
simple!
COMPUTER NETWORKS
A day in the life of a web request

## Slide 81
router has
DHCP server
arriving mobile:
DHCP client
Connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
COMPUTER NETWORKS
A day in the life of a web request

## Slide 82
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
Encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
COMPUTER NETWORKS
A day in the life : Connecting to the Internet

## Slide 83
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
Before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
Client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply
COMPUTER NETWORKS
A day in the life…. ARP (Before DNS, Before HTTP)

## Slide 84
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
Demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
COMPUTER NETWORKS
A day in the life…. Using DNS

## Slide 85
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
To send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
Web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)
COMPUTER NETWORKS
A day in the life…. TCP Connection carrying HTTP

## Slide 86
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
Web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
COMPUTER NETWORKS
A day in the life…. HTTP Request / Reply

## Slide 87
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 88
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 89
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
  Purpose, Signals to Packets
  Analog Vs Digital Signals
  Transmission Media
Wireless LANs: IEEE 802.11

## Slide 90
COMPUTER NETWORKS
Purpose
Signals to Packets
Class 53 : Intro to Physical layer : Learning Objectives

## Slide 91
COMPUTER NETWORKS
Physical layer
The Physical layer consists of hardware, in the form of
electronic circuitry,
media, and
connectors.

## Slide 92
COMPUTER NETWORKS
Physical Layer
Purpose:
Primary Purpose:
  Representation of the bits of a frame on the media in the form of signals
The physical media and associated connectors
Encoding of data and control information
Transmitter and receiver circuitry on the network devices
Each medium has a unique method of representing bits (signaling):

## Slide 93
COMPUTER NETWORKS
Physical Layer
Determine
Physical and electrical properties of the media
Mechanical properties (materials, dimensions, pinouts) of the connectors
Bit representation by the signals (encoding)
Definition of control information signals
Hardware components such as
network adapters (NICs),
interfaces and connectors,
cable materials
cable designs

## Slide 94
COMPUTER NETWORKS
Physical Layer

## Slide 95
COMPUTER NETWORKS
Physical layer Fundamental Principles
The physical components
Data encoding
Signaling

## Slide 96
COMPUTER NETWORKS
Physical Signaling and Encoding : Representing Bits
Signaling Bits for the Media
All communication from the human network becomes binary digits, which are transported across the physical media
  Transmission occurs as a stream of bits sent one at a time
  Each of the bits in the frame represented as a signal
  Each signal has a specific amount of time to occupy the media
    This is referred to as its bit time

## Slide 97
COMPUTER NETWORKS
Data Carrying Capacity
Bandwidth(Theoretical)
The capacity of a medium to carry data in a given amount of time
Takes into account the physical properties of the medium and the signaling method

## Slide 98
COMPUTER NETWORKS
Data Carrying Capacity
Throughput(Practical):
Transfer rate of data over the medium
Factors that affect: Amount and type of traffic, number of devices
Goodput( Qualitative):
Transfer rate of actual usable data bits
Throughput less the data protocol overhead, error corrections and retransmissions

## Slide 99
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 100
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 101
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
  Purpose, Signals to Packets
  Analog Vs Digital Signals
  Transmission Media
Wireless LANs: IEEE 802.11

## Slide 102
COMPUTER NETWORKS
Analog Vs Digital Signals
Transmission Media
Class 54 : Physical layer : Learning Objectives

## Slide 103
COMPUTER NETWORKS
Analog Vs Digital Signals
If data is to be transmitted, then it must be transformed to electromagnetic signals.
  Analog signals - infinite number of values in a range;
  Digital signals can have only a limited number of values.
Data can be analog or digital.
  Analog data - information that is continuous;
    Analog data example: voice temperature captured by analog sensor
  Digital data - information that has discrete states.

## Slide 104
COMPUTER NETWORKS
Transmission Media
Transmission medium-the physical path between transmitter and receiver.
Repeaters or amplifiers may be used to extend the length of the medium.
Communication of electromagnetic waves is guided or unguided.
  Guided media : waves are guided along a physical path (e.g, twisted pair, coaxial cable and optical fiber).
  Unguided media: means for transmitting but not guiding electromagnetic waves (e.g., the atmosphere and outer space).

## Slide 105
COMPUTER NETWORKS
Types of Physical Transmission Media
Twisted pair
Coaxial cable
Optical fiber
Wireless communications

## Slide 106
COMPUTER NETWORKS
Types of Physical Transmission Media

## Slide 107
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 108
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
  Purpose, Signals to Packets
  Analog Vs Digital Signals
  Transmission Media
Wireless LANs: IEEE 802.11

## Slide 109
COMPUTER NETWORKS
Why, What- Wireless LAN
802.11 Architecture
Class 55 : IEEE 802.11- Wireless LAN : Learning Objectives

## Slide 110
COMPUTER NETWORKS
Wireless LAN
Network connectivity to the legacy wired LAN
Desktop
with PCI 802.11 LAN card
Laptop
with PCMCIA 802.11 LAN card
Provides network connectivity over wireless media
An Access Point (AP) is installed to act as Bridge between Wireless and Wired Network
The AP is connected to wired network and is equipped with antennae to provide wireless connectivity

## Slide 111
COMPUTER NETWORKS
Wireless LAN
Range ( Distance between Access Point and WLAN client) depends on
  structural hindrances and
  RF gain of the antenna at the Access Point
To service larger areas, multiple APs may be installed with a 20-30% overlap
A client is always associated with one AP and when the client moves closer to another AP, it associates with the new AP (Hand-Off)

## Slide 112
COMPUTER NETWORKS
IEEE 802.11- Wireless LAN
IEEE 802.11 defines
MAC protocol and
Physical medium specification
for wireless LANs

## Slide 113
COMPUTER NETWORKS
IEEE 802.11- Terminology

## Slide 114
COMPUTER NETWORKS
Basic Service Set
BSS- Smallest building block
  Number of stations
  Same MAC protocol
  Competing for access to same shared wireless medium
May be isolated or connect to backbone distribution system (DS) through access point (AP)
  AP functions as bridge

## Slide 115
COMPUTER NETWORKS
IEEE 802.11
MAC protocol may be distributed or controlled by central coordination function in AP
BSS generally corresponds to cell
Distributed System can be switch, wired network, or wireless network

## Slide 116
COMPUTER NETWORKS
Extended Service Set
An Access Point (AP) broadcasts is SSID (service set identifier) roughly every 100 ms and at 1 Mbps (to accommodate the slowest client)

## Slide 117
COMPUTER NETWORKS
IEEE 802.11 Architecture
FHSS - frequency hopping spread spectrum
DSSS - direct sequence spread spectrum
OFDM - orthogonal frequency division multiplexing

## Slide 118
COMPUTER NETWORKS
Access Control
How a wireless host can get access to the shared medium (air)?
The CSMA/CD algorithm does not work in wireless LANs for such reasons:
  Send and receiving signal power
  The hidden station problem prevents collision detection

## Slide 119
COMPUTER NETWORKS
CSMA/CA
DIFS: distributed
interframe space
SIFS: short
interframe space

## Slide 120
COMPUTER NETWORKS
CSMA/CA
When a station sends its RTS, it includes a time of how long it needs the medium.
Other stations then set their NAV timer to this time so they don’t transmit.
DIFS: Distributed interframe space; SIFS: short interframe space
The CTS frame in CSMA/CA handshake can prevent collision from a hidden station.

## Slide 121
COMPUTER NETWORKS
Example of Repetition Interval

## Slide 122
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 123
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 124
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
  Purpose, Signals to Packets
  Analog Vs Digital Signals
  Transmission Media
Wireless LANs: IEEE 802.11

## Slide 125
COMPUTER NETWORKS
Frame Format
Addressing Mechanism
Class 56 : IEEE 802.11- Wireless LAN : Learning Objectives

## Slide 126
COMPUTER NETWORKS
Frame Format
FC: Frame Control
D: duration of the transmission that is used to set the value of NAV
SC: sequence control: defines the sequence number of the frame to be used in flow control

## Slide 127
COMPUTER NETWORKS
Sub fields in FC field

## Slide 128
COMPUTER NETWORKS
Control Frames
FC: Frame Control
D: duration of the transmission that is used to set the value of NAV

## Slide 129
COMPUTER NETWORKS
Frames Types
1. Management - used for initial communication between
stations and access points
2. Control - used for accessing the channel (RTS) and
acknowledging frames (CTS or ACK)
3. Data - used for carrying data and control information
Values of subfields in control frames

## Slide 130
COMPUTER NETWORKS
Addresses
Note:
Address 1 is always address of next device
Address 2 is always address of previous device
Address 3 is address of final destination if not defined by Address 1
Address 4 is address of original source if not defined by Address 2

## Slide 131
COMPUTER NETWORKS
Addressing Mechanism
Case 1:
Frame is going directly from one client to another. No intervening distribution system.
To DS = 0, From DS = 0
Case 2:
To DS = 0, From DS = 1 - frame is coming from a DS (Access
Point)

## Slide 132
COMPUTER NETWORKS
Addressing Mechanism
To DS = 1, From DS = 0 - frame is going to a DS (or AP)
To DS = 1 and From DS = 1

## Slide 133
COMPUTER NETWORKS
Physical layer

## Slide 134
Principles behind data link layer services:
  Error detection, correction
  Sharing a broadcast channel: multiple access
  Link layer addressing
Instantiation, implementation of various link layer technologies
  Ethernet
  switched LANS
Synthesis: a day in the life of a web request
Intro to Physical layer and Wireless LAN
COMPUTER NETWORKS
Summary

## Slide 135
Journey down protocol stack complete
Solid understanding of networking principles, practice!
….. could stop here …. but more interesting topics!
  deep understanding of wireless
  security
COMPUTER NETWORKS
Summary

## Slide 136
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M Joshi
Department of Computer Science and Engineering